## Slide 1: In Situ-Forming Corneal Transplants
Allyson Cameron

## Slide 2: Problem Statement
Corneal blindness causes 12% of worldwide blindness1
Most commonly treated with corneal transplantation from cadaver donor
  Limited supply, shelf life
~40,000 corneal transplantations annually2
Complications3
  Inflammation, infection, bleeding, cataracts, retinal detachment, rejection, surgeon error
  1: (Fu and Hollick); 2: (Akpek); 3: (Mori et al.)

## Slide 3: Design Criteria
Biocompatibility4
Immune Response5
Thickness5
Flexibility6
Optical Properties/Transparency4
Cost7
4: (Ahearne et al.); 5: (Divakar et al.); 6: (Hamilton and Pye); 7: (Biggelaar et al.)
Notes: Immune response is important to understand and modulate to maximize healing and minimize patient suffering. Rejections are most common in the immediate aftermath of the transplantation. It can be measured with white blood cell count, which should be kept to a typical level. Biocompatibility is also critical to evaluation of the performance of corneal transplants. These transplants must mimic natural corneas as closely as possible in order to be an effective intervention. Therefore thickness should also be considered. The eyelid must be able to comfortably close around the transplant. This has historically been a big challenge for artificial corneas because they also need to maintain mechanical properties like flexibility, which is most commonly evaluated with Young’s Modulus. Transparency is, of course, critical, and can be evaluated with a transmittance test. Natural corneas allow visible light to pass through freely while minimizing ultraviolet light transmittance. Finally, the cost of this intervention should be similar to the cost of a conventional cornea transplantation from a cadaver donor. Cadaver donor corneas are still considered the gold standard, so the specific values for each of these criteria are set by a cadaver cornea.

## Slide 4: Solution Landscape – BIOKOP I8
A synthetic hydrogel keratoprosthetics
Transparent core, white porous skirt
Advantages: optical properties, flexibility, cost
Disadvantages: immune response, biocompatibility
Still in development
8: (Alió et al.)
Notes: One solution is a synthetic hydrogel keratoprosthetics called BIOKOP I, shown implanted in a patient on the right. This solution is composed of a transparent core and white microporous skirt for biointegreation. This was one of the first in situ-forming implants used, and while it showed excellent optical and mechanical properties, it came with its problems. High inflammatory and immune responses resulted in shifting of the implant, vascularization, and corneal ulcers or melting were the most common nonideal responses observed.

## Slide 5: Validation and Verification
Verification
BIOKOP I8
~36% transplantations successful after 5 years
Side effects
  Endophthalmitis (4 patients)
  Retinal detachment (3 patients)
  8: (Alió et al.)
Validation
PEG Hydrogels9
Biocompatibility study of injectable hydrogel
20 New Zealand White rabbits
Successful integration, epithelial cell migration
No increased immunological response
9: (Chun et al.)
Notes: In situ-forming corneal transplants are early in development, and significant problems with current solutions have been observed. BIOKOP I, discussed on the last slide is one of the few to have a follow-up verification study, this one conducted after 5 years. 36.3% of the original 11 transplantations were considered successful, exhibiting no shifting or adverse effects, but nearly 50% of the eyes were blind. The most common complications were endophthalmitis (severe inflammation due to infection) and retinal detachment, which was only observed in patients with severe preexisting conditions. For validation of the technology behind in situ-forming corneal transplants, we turn to a study involving New Zealand White Rabbits. One group acted as a control, while the other underwent keratectomy with collagen polyethylene glycol hydrogel. The injectable hydrogel was found to be successful in integrating with host tissue, exhibiting host epithelial cells migrating into the transplant. There was no increased immunological or inflammatory response at the injection site and intraocular pressure remained constant during the four-week evaluation period. Low expression of smooth muscle actin in the hydrogel-treated group validates the biocompatibility of in sit-forming hydrogel corneal transplants. Corneas in the hydrogel-treated group were only about 20µm thicker than in the keratectomy-only group. Finally, the hydrogels are easily modulated to control mechanical properties. The technology is valid, but more work must be done to ensure it meets patient needs.

## Slide 6: References
Ahearne, Mark, et al. “Designing Scaffolds for Corneal Regeneration.” Advanced Functional Materials, vol. 30, no. 44, Feb. 2020, p. 1908996, https://doi.org/10.1002/adfm.201908996.
Akpek, Esen. “Corneal Transplantation.” Www.hopkinsmedicine.org, www.hopkinsmedicine.org/health/treatment-tests-and-therapies/corneal-transplantation.
Alió, J. L., et al. “Five Year Follow up of Biocolonisable Microporous Fluorocarbon Haptic (BIOKOP) Keratoprosthesis Implantation in Patients with High Risk of Corneal Graft Failure.” The British Journal of Ophthalmology, vol. 88, no. 12, Dec. 2004, pp. 1585–89, https://doi.org/10.1136/bjo.2004.046375.
Chen, Fang, et al. “In Situ-Forming Collagen-Hyaluronate Semi-Interpenetrating Network Hydrogel Enhances Corneal Defect Repair.” Translational Vision Science & Technology, vol. 11, no. 10, 3 Oct. 2022, p. 22, pubmed.ncbi.nlm.nih.gov/36239965/, 10.1167/tvst.11.10.22. Accessed 18 Oct. 2022.
Chun, Yoon Hong, et al. “In Vivo Biocompatibility Evaluation of in Situ-Forming Polyethylene Glycol-Collagen Hydrogels in Corneal Defects.” Scientific Reports, vol. 11, Dec. 2021, p. 23913, https://doi.org/10.1038/s41598-021-03270-3.
“Corneal Transplant Market [4.8% CAGR] 2022 Share, Upcoming Trends, Size, Key Segments, Growth Status and Forecast 2028.” MarketWatch, 30 Sept. 2022,
Divakar, Prajan, et al. “Quantitative Evaluation of the in Vivo Biocompatibility and Performance of Freeze-Cast Tissue Scaffolds.” Biomedical Materials (Bristol, England), vol. 15, no. 5, July 2020, p. 055003, https://doi.org/10.1088/1748-605X/ab316a.
Fu, Lanxing, and Emma J. Hollick. “Artificial Cornea Transplantation.” PubMed, StatPearls Publishing, 2021, pubmed.ncbi.nlm.nih.gov/33760451/. Accessed 2 Nov. 2021.
Gholampour, AhmadReza, and Hossein Jamali. “Indications and Surgical Techniques for Corneal Transplantation at a Tertiary Referral Center.” Journal of Ophthalmic and Vision Research, vol. 14, no. 2, 2019, p. 125, https://doi.org/10.4103/jovr.jovr_92_18.
Hamilton, Kirsten E., and David C. Pye. “Young’s Modulus in Normal Corneas and the Effect on Applanation Tonometry.” Optometry and Vision Science, vol. 85, no. 6, June 2008, pp. 445–50, https://doi.org/10.1097/OPX.0b013e3181783a70.
Holland, Gráinne, et al. “Artificial Cornea: Past, Current, and Future Directions.” Frontiers in Medicine, vol. 8, 12 Nov. 2021, 10.3389/fmed.2021.770780. Accessed 19 Oct. 2022.
Lee, Hyun Jong, et al. “Bio‐Orthogonally Crosslinked, in Situ Forming Corneal Stromal Tissue Substitute.” Advanced Healthcare Materials, vol. 7, no. 19, 14 Aug. 2018, p. 1800560, 10.1002/adhm.201800560. Accessed 31 Oct. 2021.
Martola, Eeva-Liisa. “Central and Peripheral Corneal Thickness.” Archives of Ophthalmology, vol. 79, no. 1, Jan. 1968, p. 28, https://doi.org/10.1001/archopht.1968.03850040030009.
McAlinden, Colm. “Corneal Refractive Surgery: Past to Present.” Clinical and Experimental Optometry, vol. 95, no. 4, June 2012, pp. 386–98, https://doi.org/10.1111/j.1444-0938.2012.00761.x.
McGhee, Charles NJ, et al. “A Brief History of Corneal Transplantation: From Ancient to Modern.” Oman Journal of Ophthalmology, vol. 6, no. 4, 2013, p. 12, 10.4103/0974-620x.122289.
Mori, Daniel N., et al. “Inflammatory Triggers of Acute Rejection of Organ Allografts.” Immunological Reviews, vol. 258, no. 1, 11 Feb. 2014, pp. 132–144, 10.1111/imr.12146. Accessed 22 Jan. 2021.
Nair, Ashwin, and Liping Tang. “Influence of Scaffold Design on Host Immune and Stem Cell Responses.” Seminars in Immunology, vol. 29, 1 Feb. 2017, pp. 62–71, www.sciencedirect.com/science/article/pii/S1044532316300781?via%3Dihub, 10.1016/j.smim.2017.03.001. Accessed 18 Oct. 2022.
van den Biggelaar, Frank J. H. M., et al. “Economic Evaluation of Deep Anterior Lamellar Keratoplasty versus Penetrating Keratoplasty in the Netherlands.” American Journal of Ophthalmology, vol. 151, no. 3, Mar. 2011, pp. 449-459.e2, https://doi.org/10.1016/j.ajo.2010.09.012.